RTL to ASIC System Design Flow using the OSU Library
Kevin Patel

---
Assumptions
RTL = VHDL or Verilog
Technology = 180nm TSMC
Currently, there are no memory models. Memory model shells are available (based on estimates from the CACTI 3.0 tool)

---
Basic Flow
RTL + Constraints
Synopsys DC
OSU Standard Cell
Library
Verilog Netlist
Constraints
Cadence SOC
Encounter
GDSII netlist
Post-extracted + Verilog netlist

---
Verification and Power Estimation
Test bench and
other supporting files
(vhdl)
+ OSU std
cell library
    (vhdl)
Verilog netlist +
Modelsim
vcd file
Cadence
SOC Encounter
power.report